Mouse Ruler
Oleksandr Sapalov
Anastasiia Stepanova
Lab training - Embedded systems - design and implementation

---
Mouse Ruler – task description
Hack a provided PS/2 Mouse. Use the movement data to measure a distance, use the two mouse buttons to start/stop/pause measurement. Print the measured distance onto an arduino display shield. Give the possibility to calculate distances and the areas of rectangles. Usage of the final project should be intuitive.

---
Mouse Ruler – required materials
The following material are required:
Arduino board
Display with 2 or 4 lines
PS/2 mouse
Extension board (contacts board)

---
Mouse Ruler – application’s logic
Application will work in 2 modes:
1. Distance measurement:
One click on left mouse button – start distance measurement.
Second click on left button – stop distance measurement and show result
One click on right mouse button – pause measurement (and show result)
Second click on right mouse button – continue measurement
2. Rectangle area’s measurement:
Click on left mouse button and hold – start measurement of rectangle diagonal
Release left mouse button – show calculated area.

---
Mouse Ruler – implementation plan
The following steps are expected to be done for implementation:
1. Basic knowledge for work with Arduino board and IDE (2 weeks).
2. Understanding of PS/2 protocol for communication with mouse and implementation of basic mouse movement/clicks detection software block (3 weeks)
3. Understanding of protocol for Display board and implementation of software block for Display (2 weeks)
4. Implementation of distance measurement SW block (2 weeks)
5. Implementation of surface measurement SW block (2 weeks)
6. Testing and acceptance of complete SW (2 weeks)
Overall required time 13 weeks

---
Mouse Ruler – the end
Thank you